## Slide 1
HSCC/ICCPS 2026
P-V2B : A Neuro-Symbolic Framework for Leveraging User Persistence in Vehicle-to-Building Charging
Rishav Sen · Fangqi Liu · Jose Paolo Talusan · Ava Pettet · Yoshinori Suzue · Ayan Mukhopadhyay · Abhishek Dubey
Vanderbilt University · Nissan Advanced Technology Center - Silicon Valley
Thanks to our collaborators at Nissan Advanced Technology Center - Silicon Valley.
Work supported in part by the National Science Foundation.
Notes: Hi everyone — I'm going to tell you about P-V2B, a neuro-symbolic framework for controlling EV charging in commercial buildings. This is joint work with my collaborators at Vanderbilt and Nissan. The headline idea is simple: the people who plug in at your office tomorrow are probably the same people who plugged in today — and if you know that, you can be a lot smarter about how you charge their cars. I'll explain why that matters, why prior work missed it, and how we turned it into a real-time controller that gets close to the offline optimum.

## Slide 2
SUPPLY–DEMAND MISMATCH
ESCALATING ENERGY COSTS
MOTIVATION
The Grid is under pressure
The Missing Piece Is Not the Hardware - EVs can serve as mobile batteries.
Every major city has EVs with 60–130 kWh of usable battery sitting idle most of the day.
02 / 26
Notes: Maarten: (~1 min)
Let's start with why this matters. Power grids are under growing strain from multiple directions.
First, there's a fundamental mismatch — solar generates the most energy midday when demand is lowest, then drops off right when evening demand ramps up. That creates the famous 'duck curve.’
Meanwhile, electricity costs have climbed roughly 50% in just six years — from about 10.5 cents per kilowatt-hour in 2019 to over 15.6 cents in 2025.

## Slide 3
03 / 26
THE VEHCILE to BUILDING (V2B) SETUP
EVs are (uncertain) mobile batteries for a building.
1
Users arrive, have an expected behavior , and provide requirements .
2
Connect to Chargers (unidirectional & bidirectional).
3
The controller sets a charging rate for every EV every time step minutes, subject to user, charger and grid constraints.
4
Objective: flatten the building load to cut the monthly electricity cost without affecting any user’s EV usage.
From Grid
From EV
Bi-directional
Req. SoC
Departure window
Bi-directional
Req. SoC
Departure window
Notes: Now here's the setup. You have a building, you have the grid feeding it, and you have a fleet of EVs that show up with bidirectional chargers. The user tells the system: I need this much charge by this time. The controller decides how fast to charge each car, and critically, when to discharge them back into the building. The goal is to flatten the load curve — pull energy from the grid when demand is low, and push it back from the EVs when the building would otherwise spike. That's vehicle-to-building, or V2B.

## Slide 4
Vehicle-to-Building (V2B) Problem: Goals
Off-peak
Peak hour
Building
Power
Off-peak
EV stay duration
Peak Building Load
Charging
Rate
Charging
Rate
0
0
ELECTRICITY COST
04 / 26
Off-Peak Rate: $0.1/kWh
Peak Hour Rate: $0.2/kWh
Demand Charge: $12/KW
1) Energy cost = $/kWh
2) Demand charge = Peak Power draw $/kW
Electricity Cost depends on:
Off-peak
Peak hour
Off-peak
Total Power
(Building
+Chargers)
0
Optimized Peak
Peak Building Load
Notes: in a way that minimizes the total electricity bill. The bill has two parts: energy cost for energy consumption for the building and EVs, and demand charges, which depend on the peak power draw in peak hours during the billing period. At the same time, we need to make sure all EV charging needs are met.
--------------------
Addressing this problem presents several challenges. Real-time decision-making is required in an uncertain environment with varying EV arrivals, charging needs, and building loads over time, making offline optimization and simple heuristics ineffective.
Additionally, decisions must be made in a continuous action space while optimizing long-term rewards, such as minimizing monthly demand charges. Traditional RL methods, designed for simpler environments with discrete actions, struggle with these complexities and face the curse of dimensionality at scale.
-----------------------
Traditional energy distribution is centralized
But with the addition of distributed energy resources transferring energy back to the main grid became is an option.
This also provides the opportunity for transferring energy directly between agents.

## Slide 5
05 / 26
THE PROBLEM
Demand charges dominate commercial electricity bills.
30%+
of a commercial building's monthly electricity bill comes from sudden power spikes (demand charges).
The operators are charged for:
how much energy is used.
single highest moment of use.
One bad afternoon leads to a much higher costs for the entire billing cycle.
[1] NREL: Identifying Potential Markets for Behind-the-Meter Battery Energy Storage: A Survey of U.S. Demand Charges
[2] LBNL: Exploring Demand Charge Savings from Commercial Solar
Notes: So why should you care about peaks? For commercial and industrial buildings, your electricity bill has two pieces: the energy you use, and one number — the single highest kilowatt spike in a given month. That single moment can account for more than 30% of the bill. One bad afternoon can cost you as much as everything else combined. So if you can shave that peak — even by a little — the financial impact is huge. This is what's called the demand charge, and it's the thing we're really optimizing against.

## Slide 6
Our V2B Research
2024
SMARTCOMP
2025
ICCPS
2025
AAMAS★
★ = Nominated for Best Paper (Top 5)
OPTIMUS
Discrete V2B Simulation
platform
DG-MCTS
Online, robust
Decision-making without training
RL-V2B
Fast, online, constrained decisions under sparse rewards
Simulation → Online Control → Learning
V2B PROGRESS
2026
ICCPS
2026
AAMAS (accepted)
P-V2B
Neuro-Symbolic
MPV + VF control
CONSENT
User
Negotiation with guarantees
Focus now on Human in the Loop
06 / 26

## Slide 7
Additional Strategies: Human in the Loop
Building/
Operator
$
EV User
Shared savings through negotiated contracts
Same employee, same car, predictable pattern
→ Personalized schedules yield deeper savings
P-V2B: Neuro-Symbolic Control with Persistence
ICCPS 2026
CONSENT: Human-Centered Negotiation
AAMAS 2026 (accepted)
Mon
Tue
Wed
Thu
Fri
User Negotiation
EV users have flexibility — tap into it
Share savings cooperatively: operator & user both profit
Unlock savings that conservative optimization misses
Employee Persistence
Same employees, same cars, day after day
Predictable patterns = deeper optimization potential
Personalized schedules per user profile
V2B RESEARCH PROGRESS
07 / 26
Notes: Abhishek
"We also realized that in a workplace setting, the same employees bring the same cars day after day."
"Those predictable patterns unlock deeper optimization — personalized schedules per user profile that compound savings over time."
"This became P-V2B, our neuro-symbolic control system with persistence, accepted at ICCPS 2026."

## Slide 8
08 / 26
THE GAP
Transient-fleet (No Persistence)
Prior V2B work treats every day as an island. Each EV’s arrival SoC is not related to its past activity.
[1] Tanguy, et al. "Optimization model and economic assessment of collaborative charging using Vehicle-to-Building." Sustainable Cities and Society 26 (2016
[2] Sen, et al. “Online decision-making under uncertainty for vehicle-to-building systems”, ICCPS 2025
[3] Liu, et al. “Reinforcement learning-based approach for vehicle-to-building charging with heterogeneous agents and long term rewards”, AAMAS 2025
No inter-day Coupling
Sampled arrival SoC
Notes: Here's where we differ from prior work. Almost every published V2B controller treats the problem one day at a time. A car arrives, they solve a daily optimization, the car leaves, they throw away state, and the next day starts fresh. This is called the transient-fleet assumption. It's tractable, but it assumes every EV is a stranger.
Existing Approaches? Before our work
Our work (CPS problem with online decision making) (brief recap)
Missing - > Ignored human element,: i. realize employees come back (actions today -> impact tomorrow)
Negotiation with humans –(CONSENT, give QR code, tbd at AAMAS )
Next->

## Slide 9
09 / 26
THE APPROACH
SoC carries across. Each EV’s arrival SoC is related to its last charging, and off-site use.
Mon
Tue
Wed
Thu
Fri
Additional block for Persistence
Persistent EV fleet
Notes: Here's where we differ from prior work. Almost every published V2B controller treats the problem one day at a time. A car arrives, they solve a daily optimization, the car leaves, they throw away state, and the next day starts fresh. This is called the transient-fleet assumption. It's tractable, but it assumes every EV is a stranger.

## Slide 10
10 / 26
THE OPPORTUNITY
Non-Persistent EV fleet, 1 building.
Example: Without Persistence in V2B (oracle solution)
building load + V2B controller output · 15-min
building only
D-MILP
daily oracle
D-MILP peak = 188kW
Combined Power use (kW)
Notes: So our answer is a neuro-symbolic hybrid. The symbolic half is a Monte Carlo Model Predictive Controller — it looks ahead to the end of the day, enforces all the physical and user constraints, and handles uncertainty by averaging over sampled futures. The neural half is a learned value function that estimates the cost-to-go from the end of the day all the way to the end of the billing cycle. The MPC gets the short-horizon feasibility right; the value function supplies the long-horizon strategy. They talk to each other through a terminal cost in the MPC objective.

## Slide 11
11 / 26
THE OPPORTUNITY
Persistent EV fleet, 1 building.
Example: Effect of Persistence in V2B (oracle solutions)
building load + V2B controller output · 15-min · kW
D-MILP
daily oracle
P-MILP
monthly oracle
P-MILP peak = 165kW
Pre-charge more on Monday & Tuesday Discharge heavily on Thursday & Friday
D-MILP peak = 188kW
Gap: 23kW
Combined Power use (kW)
Notes: So our answer is a neuro-symbolic hybrid. The symbolic half is a Monte Carlo Model Predictive Controller — it looks ahead to the end of the day, enforces all the physical and user constraints, and handles uncertainty by averaging over sampled futures. The neural half is a learned value function that estimates the cost-to-go from the end of the day all the way to the end of the billing cycle. The MPC gets the short-horizon feasibility right; the value function supplies the long-horizon strategy. They talk to each other through a terminal cost in the MPC objective.

## Slide 12
12 / 26
THE OPPORTUNITY
Daily decomposition is a strict subset of monthly control.
THEOREM
Total cost under Persistence
≤
The optimal persistent-fleet cost is never worse than the optimal daily-decomposed cost and is generally strictly better.
i.
Every daily-feasible plan is also monthly-feasible, so 𝒜D ⊆ 𝒜P.
ii.
The monthly objective minimises over a strictly larger set of strategies.
iii.
Therefore the gap εmodel = ΦD⋆ − ΦP⋆ ≥ 0 is structural, not algorithmic.
Total Cost under daily-decomposition
ΦP⋆
ΦD⋆
HOW THE CONTROLLERS COMPARE
No amount of better daily policies can close εmodel . We have to change the scope of the controller.
$9,791
$10,058
$267
Experimentally,
Notes: Of course, actually solving this online is hard for three reasons. First, everything is stochastic — arrivals, departures, building load. Second, decisions are coupled across days — what you do Monday changes what's feasible Friday, which means the reward is delayed by up to a month. And third, the action space is continuous and high-dimensional — you're setting a charging rate for every car at every fifteen-minute interval. Classical RL struggles with delayed rewards. Classical MPC can't see past its horizon. Neither alone is enough.

## Slide 13
13 / 26
THE CHALLENGES
Three challenges for online control.
01
Stochastic users and stochastic loads.
Arrivals, departures, charging needs, and building load all have uncertainty.
Deterministic MPC and heuristics degrade under noise.
Aleatoric + Epistemic uncertainty
02
Long term rewards.
One demand-charge signal. Revealed once per month.
Today's decision changes next week's feasible set: RL-style credit assignment is brittle.
Horizon = 30 days × 96 steps
03
Continuous, high-dimensional actions.
Decide charging rate per EV per 15 minutes.
Policy search and tree search both struggle on the dimensionality.
15 chargers × [-20kW, 20 kW]
Notes: So our answer is a neuro-symbolic hybrid. The symbolic half is a Monte Carlo Model Predictive Controller — it looks ahead to the end of the day, enforces all the physical and user constraints, and handles uncertainty by averaging over sampled futures. The neural half is a learned value function that estimates the cost-to-go from the end of the day all the way to the end of the billing cycle. The MPC gets the short-horizon feasibility right; the value function supplies the long-horizon strategy. They talk to each other through a terminal cost in the MPC objective.

## Slide 14
14 / 26
THE FORMULATION
A monthly MDP. The reward arrives once.
STATE · ST
Building — : peak history, current load
Chargers — : charger to EV asignment
Cars — , : energy delivered, energy required, capacity
Users — : expected future EV user behavior (arrival/departure, SoC at arrival)
REWARD · R
R = − Φtotal = − ( Σj φenergy,j + φdemand)
Φtotal is Total bill is a sum across 30 × 96 ≈ 2,880 timesteps.
φenergy,j is the energy cost (ToU charges)
φdemand is the demand charge on max. power use (wd · max j Pj), revealed at month-end.
ACTION · AT
At = {charging rate for connected EV} ∈ [rmin, rmax]
A continuous charging rate per EV, every minutes.
15 chargers × ℝ.
Notes: And that changes everything. Because now, on a low-demand Monday, you can deliberately over-charge a user's battery beyond what they asked for. That extra energy sits in their car overnight, drives home with them, comes back Tuesday morning — and now you have a pre-positioned battery ready to discharge during Friday's peak. It's a multi-day strategy that is structurally invisible to daily-decomposed controllers. We call this the Persistent V2B problem, or P-V2B.

## Slide 15
15 / 26
THE APPROACH
MC-MPC for feasibility. A learned value function for foresight.
OBJECTIVE:
System State
(load, SoC, arrivals)
Predicted
Peak monthly power
Sampling
Monte Carlo (MC) futures
Neural Value Function ()
Symbolic Monte Carlo Model Predictive Control (MC-MPC)
Maintains Physical & User constraints
Proactive Charging
Fills charging headroom below
Action
Charging/
Discharging rates for each charger
Notes: Let's unpack the MPC side. At every fifteen-minute control step, we sample ten possible futures for the rest of the day — different arrival patterns, different load realizations. We then solve one MILP that has to commit to a single first-stage action good across all ten scenarios. This is sample average approximation, and it gives us robustness against both arrival noise and load-forecast error. Constraints in this MILP guarantee every user gets the charge they asked for before they leave. Nobody's cheated out of their commute.

## Slide 16
16 / 26
THE SYMBOLIC HALF
MC-MPC: one constrained action for the current state.
Sample Average Approximation
Sample Nf futures. Solve one MILP.
Multiple trajectories per decision epoch: different arrivals, different load realizations.
A single MILP enforces identical first-stage actions across all of them.
Feasibility, not probability.
Physical constraints guarantee charging assignments & limits, maintain SoC curves.
Every user is guaranteed their required SoC at departure.
≈2 seconds per decision.
Comfortably within the 15-minute control window, and scales to 45 chargers without breaking that budget.
Horizon: end of day
samples
Nf
Notes: The value function is where the cross-day strategy lives. We don't feed it the full state — that would be enormous. Instead, we cluster users into three groups by how often they visit, and we summarize the end-of-day state with just three numbers: how much excess charge is sitting in each cluster. The VF maps those three numbers, plus the day of the month, to the expected residual demand charge. One nice engineering detail: embedding a ReLU network inside a MILP with Big-M constraints blows up to five-plus minutes per decision. So we approximate the VF with a trilinear piecewise-linear surrogate — twenty grid points per axis — and we're back down to about two seconds per decision.

## Slide 17
17 / 26
THE NEURAL HALF
The Value Function (VF) predicts the effect of actions on rest of the month.
Compact end-of-day abstraction
Cluster users into 3 groups.
Bucket by historical arrival frequency and stay duration.
For each cluster, sum the excess SoC above required levels (energy buffer).
Inputs: day, ΔE¹, ΔE², ΔE³ → residual power peak.
A small ReLU MLP (64×64), trained first on offline MILP oracle targets, then fine-tuned online.
Piecewise-linear surrogate inside the MILP.
Big-M embedding takes 5+ minutes per decision.
SOS2-based trilinear interpolation (20 grid points per axis) brings it down to ≈2 s with MAE ≈ 0.03.
Notes: Here are the peak-shaving numbers. Fast charging — the real-world baseline, just charge everyone as fast as you can — averages about 199 kilowatts. Daily RL and daily MCTS, which are the state-of-the-art online controllers, sit around 171 to 173. Our method comes in at 156, which is within about three kilowatts of the building-only profile. That means we're serving all the EV charging demand without creating a peak that's meaningfully bigger than the building would have had on its own. And we're remarkably close to the offline persistent oracle, which is 121 — that gap is the unavoidable cost of not having perfect foresight.
What is the effect of pre vs post value function?

## Slide 18: V2B Testbed: Nissan Advanced Technical Center – Silicon Valley
THE TESTBED
18 / 26
Bidirectional Chargers
Bidirectional EVs
Commercial building

## Slide 19
19 / 26
THE DATA
The same people arrive every day.
Anonymized commuter data from Nissan's Santa Clara office. A sharp morning arrival peak, and a median of 15 visits per vehicle, every month.
Arrival time distribution
discrete · binned by hour · all vehicles · 2024
Monthly visit frequency per vehicle
discrete · one point per month · median & mean · 2024
Notes: But in a real office building, the same fifteen or twenty employees show up every single day. Look at the arrival-time histogram — there's a sharp morning peak. The average car visits fifteen to twenty times per month. These aren't strangers; they're regulars. That persistence means the SoC you leave a car at on Tuesday evening is the SoC that car arrives with on Wednesday morning — minus whatever they used driving home.

## Slide 20
20 / 26
EVALUATION
A full year of real building load from Santa Clara, California.
Monthly building load profile, 2024
kW · 15-min resolution
15
Persistent users · Bidirectional chargers · 20 kW max
$0.18 / kWh
Peak time-of-use · 6 AM – 10 PM
$11.67 / kW
Demand charge during peak hours (6AM -10PM)
30 x 12 test samples
Stochastic monthly scenarios
Notes: To close: persistence is a structural feature of real office EV fleets, and ignoring it costs money. A neuro-symbolic controller — short-horizon MILP with a learned long-horizon terminal cost — gets you near-oracle performance while respecting every user's charging requirement, and it scales to larger fleets within the fifteen-minute control window. I'd love to take your questions.

## Slide 21
21 / 26
Peak Shaving
Mean monthly peak power (demand charge equivalent), averaged over 12 months (in kW)
lower is better
Notes: Thank you. Happy to take questions.

## Slide 22
22 / 26
Cost, Ablations, and Robustness
MONTHLY BILL
Lowest mean bill among all online controllers.
All user SoC requirements met, every scenario.
ROBUSTNESS
Graceful under upto 4× nominal forecast noise.
Load-forecast noise stressed to ±20%.
Ours drifts ~16 kW; MCTS drifts 50kW+.
Power (kW)
ABLATION
The VF is the dominant driver. Proactive charging helps.
Full year, mean bill. VF carries long-horizon strategy; PC builds the buffer.
MC-MPC base
+ proactive charging
+ value function (VF)

## Slide 23
23 / 26
REAL-TIME FEASIBILITY
Time to decision
Mean wall-clock per decision · 15 chargers
SECONDS · LOG SCALE
D-FC
≈ 5 ms
D-LLF
≈ 5 ms
D-RL
≈ 50 ms
MC-MPC base
≈ 1 s
MC-MPC + VF
≈ 2 s
D-MCTS
≈ 15 s
D-MCTS spends 7.5× our budget — for worse bills (slide 18).
.
2
.
Notes: A few more results worth mentioning. The dollar savings track the peak-shaving — lowest monthly bill among all online controllers. The ablation confirms that both the value function and the proactive-charging term contribute, with the VF being the dominant factor. And under load-forecast noise of plus or minus twenty percent — four times the nominal uncertainty — we only degrade by about seven dollars on the peak-power side, while MCTS degrades by fifty-plus kilowatts. That robustness comes directly from the Monte Carlo scenario sampling.

## Slide 24
24 / 26
CAVEATS
MC-MPC + VF with persistence beats other approaches, with caveats.
UNKNOWN USER
A stranger offers no usage history.
No prior operator visits means no learned persistence signal, Û, to leverage.
Fall back to MC-MPC base with conservative assumptions.
MPC+VF still ≥ MPC base once even one return visit is observed.
USER FREQUENCY
Persistence improves with repeat visits.
SUDDEN DISRUPTIONS
User leaves, charger breaks, building load spikes.
Abrupt mid-session events break the learned persistence pattern
MPC+RL still outperforms MPC-only even under disruption. The MILP layer provides a hard safety floor.
More operator history → stronger Û signal → better performance.
Infrequent users provide weak signal; the system degrades toward MC-MPC base.
Notes: MPC + RL is more robust than pure RL/MCTS. No unknown user information, and users use the operator multiple times. If a stranger comes, we need to use a very conservative assumption. Takeaway: Persistence relies heavily on user behvaior –the more the better. The less its, it boes back to the MC-MPC base. More nfo we know – better leverage better performance. User suddenly leaves, charger broken, building sddenly spikes – limitation,s but MPC+ RL still better than MPC only.

## Slide 25
25 / 26
FUTURE SCOPE
Improving Persistence with User flexibility & Demand Response
LEVERAGING THE COMPLETE PIPELINE
P-V2B + CONSENT + Demand Response (DR) Control
The works combined: P-V2B generalises across sites, CONSENT enforces per-user privacy, DR opens more scope for operator incentives, all with online decisions.
Where is this useful?
Commercial V2B deployment partner
Fleet operators & smart-parking platforms
Path from simulation to live infrastructure
Proprietary industry data: Working on planned release of open benchmark & dataset
OPEN QUESTIONS
Where we want to explore next.
Multi-site VF: shared structure across Nissan campuses
Online VF updates: react to seasonal users without retraining
Mixed fleets: P-V2B for the persistent core, RL for the transient tail
Co-optimization with on-site solar & stationary storage

## Slide 26
26 / 26
Thank you.
Questions & Comments?
rishav.sen@vanderbilt.edu
Thanks to our collaborators at Nissan Advanced Technology Center - Silicon Valley.
Work supported in part by the National Science Foundation.
Paper Link

## Slide 27: V2B RESEARCH PROGRESS
Q
Mixed Linear Programming (MILP)
MCTS: Monte-Carlo Tree Search1
Reinforcement Learning System2
Pros:
Fully online, anytime, and robust
Robust to environmental changes
Cons:
Slow, mainly due to the number of iterations
Large action space is a major challenge
Pros:
Fast Effectively address complex input features Long-Term Optimization
Cons:
Challenges with large and continuous action spaces.
Limited robustness to unseen conditions.
Pros:
  Optimal solution
Cons:
Poor at handling uncertainty
Needs complete information (Oracle)
  Fast convergence (for regular problem size)
Deterministic  Uncertainty Aware Systems
[1] Sen et. al, Online Decision-Making Under Uncertainty for Vehicle-to-Building Systems, ACM/IEEE ICCPS 2025
[2] Liu et. al, Reinforcement Learning-based Approach for Vehicle-to-Building Charging with Heterogeneous Agents and Long Term Rewards, AAMAS 2025

## Slide 28
07 / 28
THE OPPORTUNITY
Same fleet, same building. Now with persistence.
Example: Effect of Persistence in V2B (oracle solutions)
building load + V2B controller output · 15-min · kW
D-MILP
daily oracle
P-MILP
monthly oracle
P-MILP peak = 165kW
Pre-charge more on Monday & Tuesday Discharge heavily on Thursday & Friday
Gap: 23kW
Combined Power use (kW)
D-MILP peak = 188kW
Notes: So our answer is a neuro-symbolic hybrid. The symbolic half is a Monte Carlo Model Predictive Controller — it looks ahead to the end of the day, enforces all the physical and user constraints, and handles uncertainty by averaging over sampled futures. The neural half is a learned value function that estimates the cost-to-go from the end of the day all the way to the end of the billing cycle. The MPC gets the short-horizon feasibility right; the value function supplies the long-horizon strategy. They talk to each other through a terminal cost in the MPC objective.

## Slide 29
11 / 28
THE APPROACH
MC-MPC for feasibility. A learned value function for foresight.
Short-horizon MILP enforces every physical and user constraint. The neural VF plugs in as a terminal cost, carrying month-long strategy into a one-day optimization.
Notes: Let's unpack the MPC side. At every fifteen-minute control step, we sample ten possible futures for the rest of the day — different arrival patterns, different load realizations. We then solve one MILP that has to commit to a single first-stage action good across all ten scenarios. This is sample average approximation, and it gives us robustness against both arrival noise and load-forecast error. Constraints in this MILP guarantee every user gets the charge they asked for before they leave. Nobody's cheated out of their commute.

## Slide 30
17b / 26
TWO EXTRA INGREDIENTS · THE BUFFER AND THE HEADROOM
Build a buffer in the objective. Spend any leftover headroom after solving.
01 · IN THE MPC OBJECTIVE
min 𝔼F [ Σ φenergy + Φdemandteod − wpc·Σv,k rv,kj·Δt + JVF(Steod) ]
A small reward for charging beyond what the user asked for — pays for itself in a future peak.
GRID SEARCH
wpc ∈ [0, 5] · step 0.2
BEST
wpc = 0.8
02 · AFTER THE MILP SOLVES
rv,kt ← min( rv,kt + Pdiff / |Vt|, rmax ) if it doesn't violate the user's SoC cap
step 1 · proactive charging
Plant a buffer the VF will spend later.
Without a nudge, the MPC has no reason to put more into a car than the user asked for — and the cross-day buffer never forms. The −wpc ·Σ r·Δt term rewards slight overcharging during low-cost windows.
Kept small on purpose — enough to seed persistence, never enough to create a new peak alone.
step 2 · action refinement
Don't leave free headroom on the table.
MC-MPC is conservative — one action shared across ten futures. The realized load is often lower than the worst sample, leaving room under P̂max that it didn't use.
A fast heuristic spreads any positive Pdiff evenly across connected EVs, capped by charger and SoC limits. Free efficiency, by construction no new peak.

## Slide 31
22 / 28
TAKEAWAYS
Persistence is structural. Treat it as a control opportunity, not noise.
NEAR-ORACLE
<5
Lowest mean monthly bill among all online controllers, across a full year of real building load.
USER REQUESTS FULFILLED
100 %
Every user meets their required state-of-charge at departure, every scenario. MILP-enforced, not reward-tuned.
REAL-TIME SCALABLE
≈2 s
Per decision at 15 chargers; 22 s at 45 chargers: well within the 15-minute control window.
%
gap
Notes: Show how we are combining FSL+CONSENT+online decisions. How does this work combined? Where does this go? - Resilio
Mobility
Real deployment?
This is prop. industry data. Working on open dataset & benchmark (similar to MoveOD) - open source that Cheekily talk about Postdoc employment

## Slide 32
10 / 26
WHAT MC-MPC ACTUALLY SAMPLES FROM
Four conditional models for Monte Carlo sampling.
EV behavior · component models
22 MO. NISSAN TELEMETRY
RANDOM VARIABLE
MODEL FAMILY
CONDITIONED ON
Arrivals / 15 min
Zero-inflated negative binomial
Date · DoW (day of week) · Hour
Arrival SoC
Beta regression
DoW · cyclical time
Departure SoC
Beta regression
Arrival SoC · DoW · time
Stay duration
Weibull survival
DoW · arrival time
Building load
Realized load + 5% zero-mean Gaussian noise
AT CAR ARRIVAL
DRAW 1 · ZINB
arrival times of future cars
↓
DRAW 2 · BETA
Arrival SoC of future cars
↓
DRAW 3 · BETA | ARRIVAL SOC
Expected departure SoC of future cars (target the controller must hit)
↓
DRAW 4 · WEIBULL
Expected stay duration of future cars (when the car leaves)
+
BUILDING · REALIZED + NOISE
15-min load trajectory
KEY ASSUMPTION
Arrivals are exogenous. We presample once per scenario; the MILP only sets charging rates.
Validated with the building operator: schedules don't depend on building load or prior charging.

## Slide 33: BACKUP — Q&A B1 / B6 How sensitive is performance to PWL grid resolution?
20 grid points/dim = operating point: MAE ≈ 0.030–0.034, runtime ~2 s
Coarser grids → MAE degrades
Finer grids → runtime exceeds 15-min control interval
Full tradeoff table: paper Appendix
Notes: Triggered by 'why 20 grid points?' [partial — exact full tradeoff table is in paper Appendix].

## Slide 34: BACKUP — Q&A B2 / B6 How is the VF trained?
Stage 1 — Offline pre-training
Synthetic monthly scenarios → P-MILP oracle → (VFInput(S_t), Φ_demand,end − Φ_demand,eod) supervised pairs → train [64,64] ReLU MLP
Stage 2 — Online fine-tuning
Bracket MC-MPC behavior with Nominal MPC (mean forecast) + Robust MPC (95th-percentile worst-case); roll out to month-end, store realized residual demand charge in replay buffer, regress JVF toward it. Iterate.
Notes: Bracketing trick (Nominal + Robust MPC) avoids the cost of training on full MC-MPC rollouts. Replay buffer is per-month; one VF per month worked best in our sweep.

## Slide 35: BACKUP — Q&A B4 / B6 Why not month-long stochastic MPC or persistence-aware RL/MCTS?
1. Month-long stochastic MPC: 30 days × 96 timesteps × N_f scenarios × continuous action → MILP intractable; loses real-time guarantees
2. Persistence-aware RL: 2880-step episode, dominant demand-charge signal at terminal step → severe credit-assignment + exploration problems
3. Persistence-aware MCTS: continuous action × month-long horizon → branching explosion
Our hybrid sidesteps all three.
Notes: Defend by emphasizing credit-assignment in monthly-horizon RL: the dominant signal (demand charge) only shows up at month-end, after 2880 timesteps. RL needs millions of episodes to learn that. Our hybrid uses MILP for short horizon and pre-trained VF for long horizon, sidestepping the credit-assignment problem entirely.

## Slide 36: BACKUP — Q&A B5 / B6 What hyperparameters did you use?
Hyperparameter | Range / Best
F (sample size) | 5–30 (step 5) · best = 10
w_pc (proactive) | 0–5 (step 0.2) · best = 0.8
VF architectures | [16,16], [32,32], [64,64]
Learning rates | 10⁻³ – 10⁻⁵
Best VF | [64, 64], one per month
PWL grid | 20 points / dim
Action refinement on (~$80/month gain).
Notes: Grid search across F, w_pc, VF architecture, and learning rate. Per-month VF (one network per calendar month) was a meaningful gain over a single year-round VF — pre-empts hyperparameter brittleness concerns.

## Slide 37: BACKUP — Q&A B6 / B6 What about unexpected user dropout?
Dropout (Jul–Sep) | MC-MPC+VF (ours) | D-RL
5% | $13,382 ± 1,054 | $13,479 ± 1,044
10% | $13,363 ± 1,052 | $13,428 ± 1,044
Mechanism: when a user fails to arrive, the MPC layer observes zero availability and re-optimizes over the remaining fleet → immediate feasibility correction without re-training the VF.
Notes: MPC layer auto-corrects under distribution shift. The VF was trained on full-attendance assumptions, so it's wrong when users drop out — but the MPC layer absorbs the correction online by re-optimizing over the realized fleet. Cleanest illustration of why the symbolic layer matters under uncertainty.

## Slide 38
Our V2B Research Journey
2024
SmartComp
2025
ICCPS
2025
AAMAS★
OPTIMUS
Discrete-Simulation
platform
DG-MCTS
Online
Decision-making
RL-V2B
Reinforcement
Learning with sparse rewards
2026
P-V2B
ICCPS
Neuro-Symbolic
control
2026
CONSENT
AAMAS (accepted)
User
Negotiation with guarantees
★ = Nominated for Best Paper (Top 5)
Simulation → Online Control → Learning → Persistence → Human-in-the-Loop