## Slide 1
VALIANT AI DISCOVERY PITCH · 2026
Resilio
Turning EVs into on-demand
grid assets for commercial campuses & emergency response
Rishav Sen · PhD Candidate, ECE · Vanderbilt University
Fangqi Liu · Postdoc, Computer Science · Vanderbilt University
Abhishek Dubey · Associate Professor, Computer Science & Electrical and Computer Engineering · Vanderbilt University

## Slide 2
The Problem: EV Coordination & Grid Resilience
January 2026 — Nashville Ice Storm
Power knocked out for days to over a week across the city. Community spaces struggled to stay open.
Thousands
of charged EVs sat idle nearby
0 kWh
reached any resilience hub
The Missing Piece Is Not Hardware
Every mid-size US city has EVs with 60–130 kWh of usable battery sitting idle most of the day.
Current Gaps
Coordination software
Does not exist
Empirical data
No one has measured opt-in rates
Bidirectional hardware
Now shipping on consumer vehicles
Notes: Motivation & Problem
What am I tryi9ng to do
WHy is it Innovative? ( Hard)

## Slide 3
The Research Challenge
Turning a voluntary pool of EVs into a reliable energy resource requires solving four problems simultaneously.
01
Forecast
Predict which vehicles will be available and when outage demand will spike, under uncertainty.
02
Mobility Planning
Solves rolling MILP: assigns EVs to sites, sets charging rates under battery, travel, and budget constraints.
03
Charging Control
Real-time MPC controller sets charging/discharging rates for each connected EV to minimize peak demand and energy costs under hard operational constraints.
04
Pricing & Safeguards
Strategy-proof mechanism ensures truthful driver participation; hard constraint veto blocks any dispatch stranding a driver or under-serving a site before execution.

## Slide 4
AI System: Closed-Loop EV Coordination
1
Forecast (Modeling, MPC)
ITSC 2024
MC-MPC samples future EV arrivals and building loads, forecasts peak demand, plans EV dispatch under battery,budget constraints.
Validated result
Validated on 18 months live operational data, Nissan ATC Silicon Valley
2
Charging (MPC+RL)
ICCPS 2025 · ICCPS 2026
MPC+RL controller control EV charging/discharging rates to minimize demand charges and energy costs.
Validated result
Building cost reduced 5.83% vs uncoordinated charging, operator savings confirmed on real load data
3
Pricing (MC-MPC)
AAMAS 2026
Strategy-proof MDP mechanism, truthful reporting is provably dominant strategy; drivers cannot inflate earnings by misreporting.
Validated result
22% user cost reduction, reject rate 34.9%→22.0%, user cost $0.178→$0.138/kWh
The novelty is not any single layer. It is the closed-loop integration
Notes: How do we solve the Challenges in slide 3?
Add expected savings
Main challenges & techniques for each layer

## Slide 5
Goals
Phase 1 · Weeks 1–4
Data Collection
Track driving and energy usage patterns from voluntary EV users
Build Nashville’s digital twin for EV user mobility and charging/discharging simulation
Gather real-time load data from smart buildings
Phase 2 · Weeks 5–10
Model & Simulate
Build User App & Interface
Real dispatch requests via app
Drivers plug in, discharge, get compensated
Phase 3 · Weeks 11–12
Measure
Quantify User uptake
Publish dataset (open release)
Technical report for municipal planners
Notes: FInal Goal of th project
Step 1: Data Collection (a larger paid survey); EV mobility, user behavior, charger data
Step 2: Model, Interface and Simulate the policies on the combined approach & user interface.
Step 3: Involve Nissan’s EV facilities for Pilot.

## Slide 6
VALIANT AI DISCOVERY PITCH · 2026
Appendix

## Slide 7
Why Vehicle-to-Grid?
High Variable Costs
Time-of-Use rates: Energy usage prices depend on time of day (high during afternoon).
Demand Charges: A fee on the highest power drawn in a billing cycle (>30% of bill).
Vehicle-to-X: A Spectrum of Opportunities
V2B
Building peak shaving
V2H
Home backup power
V2G
Grid frequency regulation
User requirements
Each user has a Required SoC and Requested Departure.
To ensure reliability, the system must meet these requirements precisely.
EV as Battery Asset
A typical EV has ~60 kWh battery capacity.
With bidirectional chargers, each parked EV becomes an energy reserve

## Slide 8: Use Case
EV Figure Source: http://driveelectricmn.org/electric-vehicles/
Other images from flaticon: kerismaker, aldo-cervantes, freepik, vectors tank
1
2
3
Lisa and Joe carpooled to work on their electric vehicle (EV)
They use a service and enter their desired charge at departure.
Their EV is connected to an available charger
4
Building draws power from the grid, charging cars to build a reserve capacity
5
Discharge the EVs, using the reserve capacity when rates/power use is high
6
Lisa and Joe return & their EV has been charged to the required level
Cloud

## Slide 9: Why Is V2B Optimization Hard?
Uncertainty
Stochastic EV arrivals
Varying SoC needs (SoC gaps)
Departure windows
Varying building loads
Long planning horizon
Delayed rewards - Demand cost based on monthly peak power
High-Dimensional Action Space
Lots of chargers - Combinatorial explosion!
Scalability
Support varying charger counts without retraining
Notes: Departure window - in practice no one can provide exact departure time.
If you knew exactly when people arrive & depart - it can be a giant sequential opt problem, but we don't know that. People have solved using ILPs, but it is not deployable - so we don't see any large scale deployments, in a manner that is not adhoc
Combinatorial explosion::
  Action space for chargers and discrete rates
  Exploring full symmetrical search tree is practically impossible
  Given time restrictions, solution quality can be heavily affected
Once we understand the V2B problem, the real question is: why is it hard to solve?
First, uncertainty dominates—user arrivals, energy needs, and departure times are not known exactly.
Second, this isn’t just a short-horizon control problem. Demand charges are computed monthly, so early mistakes can’t be fixed easily.
Third, the action space is huge—each charger and car adds exponential complexity.
Takeaway: This slide sets up the modeling and algorithmic innovation to follow. It tells the viewer: This is not your average control problem.
Departure window - in practice no one can provide exact departure time.
If you knew exactly when people arrive & depart - it can be a giant sequential opt problem, but we don't know that. People have solved using ILPs, but it is not deployable - so we don't see any large scale deployments, in a manner that is not adhoc
Combinatorial explosion::
  Action space 𝑝^𝑁 for 𝑁 chargers and 𝑝 discrete rates
  Exploring full symmetrical search tree is practically impossible
  Given time restrictions, solution quality can be heavily affected
Once we understand the V2B problem, the real question is: why is it hard to solve?
First, uncertainty dominates—user arrivals, energy needs, and departure times are not known exactly.
Second, this isn’t just a short-horizon control problem. Demand charges are computed monthly, so early mistakes can’t be fixed easily.
Third, the action space is huge—each charger and car adds exponential complexity.
Takeaway: This slide sets up the modeling and algorithmic innovation to follow. It tells the viewer: This is not your average control problem.

## Slide 10
Research Journey: 2024 – 2026
5 publications at top venues in 2 years
2024
OPTIMUS
SmartComp
Discrete-Simulation
platform
2025
DG-MCTS
ICCPS
Online
Decision-making
2025
RL-V2B
AAMAS ★
Reinforcement
Learning with sparse rewards
2026
P-V2B
ICCPS
Neuro-Symbolic
control
2026
CONSENT
AAMAS
User
Negotiation with guarantees
Acceptance rates: 24–33% | ★ = Best Paper Nominated
Progression: Simulation → Online Control → Learning → Persistence → Human-in-the-Loop

## Slide 11
How Our Work Advances the SOTA
Our Work
Prior SOTA
Our Works →
Differentiating Dimension
Prior SOTA*
RL-V2B
AAMAS '25
DG-MCTS
ICCPS '25
P-V2B
HSCC '26
CONSENT
AAMAS '26
Heterogeneous charger fleet
Mix of uni- & bidirectional, varying power rates
✗
Homogeneous assumed
✓
Multiple types, rates
✓
Multiple types, rates
✓
Multiple types, rates
✓
Multiple types, rates
Multi-day billing horizon
Explicit 30-day demand charge optimization
~
day-ahead only
~
monthly reward
~
monthly reward
✓
cross-day value fn
✓
cross-day via MPC
Formal incentive guarantees
Strategy-proof & budget-feasible mechanism
✗
✗
✗
✗
✓
proven theoretical guarantees
Technical precision dimensions ↓
Algorithm paradigm
Core method for action selection
LP / MIP
offline, static
DDPG
continuous RL
DG-MCTS
online tree search
MC-MPC + VF
neuro-symbolic
MC-MPC + Negotiation
mechanism design
Domain-aware training
MILP or domain heuristics guide learning
✗
pure solver / RL
✓
MILP policy guidance
✓
domain-pruned tree
✓
MC sampling + NN
~
MPC-structured
Online EV arrival uncertainty
Decisions without knowing future arrivals
~
forecast-based
~
model-free RL
✓
online w/ pruning
✓
MC over futures
✓
realtime MPC
Cross-day coordination
Actions today affect next day's cost
✗
greedy / daily
✗
no explicit model
✗
no explicit model
✓
Long term value function
✗
*references at the end

## Slide 12
OPTIMUS: The Simulation Foundation
IEEE SmartComp 2024 • Talusan, Sen, Pettet et al.1
What is OPTIMUS?
A discrete-event simulation platform built on real Nissan data that provides a shared sandbox for benchmarking V2B optimization algorithms.
Generative models from real EV & building data
Modular: swap policies, charger configs, grid events
Built-in MILP, MCTS, RL, and greedy solvers
Web dashboard for non-technical users
API for real-time charger integration
Architecture
Data Collection
Generative Models
Policy Engine
Dashboard UI + API
[1] OPTIMUS: Discrete Event Simulator for Vehicle-to-Building Charging Optimization. SMARTCOMP 2024, J.P. Talusan, R. Sen, A. Pettet, A. Kandel, Y. Suzue, L. Pedersen, A. Mukhopadhyay, A. Dubey (2024).– Simulator to evaluate V2B optimization algorithms at scale.

## Slide 13
Solution Approaches & Priors
[3] Tanguy, Kevin, et al. "Optimization model and economic assessment of collaborative charging using Vehicle-to-Building." Sustainable Cities and Society 26 (2016): 496-506.
[4] Nakahira, Yorie, et al. "Smoothed least-laxity-first algorithm for EV charging." Proceedings of the Eighth International Conference on Future Energy Systems. 2017.
Myopic Greedy Policies
Fast approximate heuristics
Greedy
Cars charged to required SoC only (no discharging); chargers turn off once satisfied.
Schedule-Based
Charge based on available capacity above a threshold; discharge when resources allow to stay below demand limit.
Deterministic Problem
Full future knowledge assumed (oracle)
LP modeling3
Branch & bound via off-the-shelf solvers; scales to ~200 vehicles over the 30-day billing horizon.
Large-scale heuristic
Custom heuristics like Least Laxity First4 for fleets beyond solver capacity.
Requirement: complete future knowledge
MILP modeling
Includes added complexity; allows binary decisions
Stochastic Problem
Online; uncertain arrivals and prices
Challenge
Sparse rewards and high-dimensional action space make standard RL methods difficult to apply directly.
Our approach
Non-myopic methods with domain-specific modifications: action masking, MILP guidance, MC tree search, and neural value functions.
Key research frontier

## Slide 14
Reinforcement Learning for V2B
AAMAS 2025 • Liu, Sen, Talusan et al.5 • Best Paper Nominated • Acceptance: 24.5%
Enhanced DDPG Framework
Handles sparse rewards arriving at end of monthly billing period
Action masking: domain-specific constraints ensure feasible charger actions
MILP-driven policy guidance during training for faster convergence
Handles heterogeneity in chargers (uni- & bidirectional) with varying rates
Validated on 9 months of real Nissan operational data
Key Results
Significant cost savings (>4%)
over heuristic and traditional RL baselines across all months, meeting 100% of EV charging requirements
Scalable approach
One of the first general, scalable solutions for V2B energy management: handles real-world heterogeneity and long-term reward horizons
[5] Reinforcement Learning-based Approach for Vehicle-to-Building Charging with Heterogeneous Agents and Long Term Rewards. AAMAS 2025, F. Liu, R. Sen, J.P. Talusan, A. Pettet, A. Kandel, Y. Suzue, A. Mukhopadhyay, A. Dubey

## Slide 15: Online Decisions under Uncertainty: DG-MCTS
Handles Uncertainty, Plans Non-Myopically, Provides near-optimal actions, Scales Efficiently
1. Gather exploration samples (EVs and building loads)
2. Estimate peak power (using MILP in exploration samples).
3. Pruned actions
(domain heuristics + power gap actions)
4. MCTS evaluates actions, simulates with trickle charging policy.
5. Select best action from averaged root-parallel trees.
At each time step,
IEEE/ACM ICCPS 2025 • Sen, Zhang, Liu et al.6 • Acceptance: 26%
Extension: Decentralized DG-MCTS scales linearly, for small performance tradeoff
DG-MCTS lowest in 6 of 8 months (~3 % cheaper than RL)
Lower price increase under more uncertainty (building load & EV user behavior)
SoC requirements are kept flexible
Key Results:
[6] Online Decision-Making Under Uncertainty for Vehicle-to-Building Systems. ICCPS 2025. R. Sen, Y. Zhang, F. Liu, J.P. Talusan, A. Pettet, Y. Suzue, A. Mukhopadhyay, A. Dubey
Notes: Very quick summary
Step 1: Links to stochastic EV arrivals (uncertainty)
Step 2: Reuses MILP for offline peak estimation
Step 3: Comes from the action space reduction slide
Step 4–5: Comes from the “how MCTS works” explanation
Speak only the bold parts of the features

## Slide 16
P-V2B: Neuro-Symbolic Control with Persistence
Key Insight:
Employees return daily, exploit this persistence to plan multi-day charging strategies.
Enables Over‑charges during low demand, enabling deeper discharge during peak days.
MC-MPC Layer (Short-horizon symbolic optimizer)
Monte Carlo sampling over N samples of EVs & building load
Solves MILP per step across N samples, till end of day
Embeds neural VF via PWL for tractable real-time actions
Guarantees feasibility and all user SoC requirements
Neural Value Function (VF) (Long-horizon learned predictor)
Input: {day, overcharge user clusters} at end of day
Predicts monthly peak power; trained offline on MILP
Online fine-tuning via replay buffer; surrogate aligns VF with MC-MPC behavior over time
Enables cross-day coordination (proactive overcharging) that no single-day solutions can achieve
Formal Guarantee
The persistent formulation provably achieves lower or equal cost than any daily-decomposed policy
IEEE/ACM ICCPS 2025 • Sen, Liu, Talusan et al.7. • Acceptance 25%
Policy
Peak (kW)
Bill ($/mo)
vs Ours
MC-MPC+VF (Ours)
156 ± 3
$10,238
—
D-RL (DDPG)
171 ± 9
$10,392
+1.5%
D-MCTS
173 ± 4
$10,439
+2.0%
D-LLF heuristic
184 ± 4
$10,557
+3.1%
Fast Charging
199 ± 4
$10,732
+4.8%
Annual Performance
[7] Sen, Rishav, et al. "P-V2B: A Neuro-Symbolic Framework for Leveraging User Persistence in Vehicle-to-Building Charging." Accepted to ICCPS (2026).

## Slide 17
CONSENT: Human-Centered Negotiation
AAMAS 2026 • Sen, Liu, Talusan et al.8 • Acceptance: 25%
Moving beyond pure optimization: negotiating with real humans to align building and driver incentives.
Features:
  Explicitly models user flexibility (departure time, SoC).
  Reward heterogeneity in user flexibility (minor deviations in SoC, departure times).
Solution:
  Stochastic MPC charging & Negotiation policies (interdependent)
Guarantees:
  Strategy-proof (cannot be gamed)
  Budget-feasible (incentives are capped at expected savings)
  Voluntary participation (Every user benefits from participating)
Results:
  Operator cost ↓ ~6%; User cost ↓ ~22%.
  Sustains ~78% participation of test users.
Novelty: Option generation & Cost evaluation for options
[8] Sen, Rishav, et al. "CONSENT: A Negotiation Framework for Leveraging User Flexibility in Vehicle-to-Building Charging under Uncertainty." Accepted to AAMAS (2026).
1
Users arrive at work on their EVs
4
Connect their EV to a charger, expecting desired charge level by departure
2
They enter:
Departure time
Requested SoC
Cloud
5
Chargers charge/discharge EVs to meet desired charge
PRICE OPTIONS
Select & Charge
Recommended choice 1: $
45%
6pm
5:30pm
Recommended choice 2: $
55%
6pm
4:30pm
User chosen: $
6pm
3:15pm
Reject All
3
Our Contribution
60%

## Slide 18
What's Next
PRIMARY OPEN PROBLEMS
01
Grid Integration
V2G Aggregation & Demand Response
Single-building DR signals
Respond to utility demand response events in real time while guaranteeing user SoC: no existing framework handles persistent users under DR.
Multi-building aggregation
Coordinate fleets across buildings as a virtual power plant; requires decentralized control that preserves cross-day coupling and fairness.
Multi-stakeholder incentives
Utility, operator, and user objectives conflict: mechanism design for three-way incentive alignment is formally open.
02
AI / Forecasting
Foundation Models for V2X Forecasting
Zero-shot arrival & load prediction
LLMs and time-series foundation models (e.g., TimesFM, Moirai) could generalize across buildings without site-specific retraining.
Embedding behavioral persistence
Current models treat time series as stationary; encoding user identity across sessions is an open architectural challenge.
Forecast-to-control pipeline
Tight integration of foundation model outputs into MC-MPC scenario sets — calibration and uncertainty quantification remain unsolved.
SUPPORTING CHALLENGES
Sim-to-Reality Gap
Standards & Adoption
Battery Degradation
Open Benchmark Dataset

## Slide 19
[9] Sivagnanam, Amutheezan, et al. "Minimizing energy use of mixed-fleet public transit for fixed-route service." Proceedings of the AAAI Conference on Artificial Intelligence. Vol. 35. No. 17. 2021.
[10] Tang, Wanrong, and Ying Jun Zhang. "A model predictive control approach for low-complexity electric vehicle charging scheduling: Optimality and scalability." IEEE Transactions on Power Systems 32.2 (2016): 1050-1063
[11] Orfanoudakis, Stavros, et al. "Scalable reinforcement learning for large-scale coordination of electric vehicles using graph neural networks." Communications Engineering 4.1 (2025): 118.
[12] Yee, Timothy, et al. "Monte Carlo Tree Search in Continuous Action Spaces with Execution Uncertainty." IJCAI. 2016.
[13] Yang, Shaobing, Shanshan Zhang, and Jingjing Ye. "A novel online scheduling algorithm and hierarchical protocol for large-scale electric vehicle charging coordination." IEEE Access 7 (2019): 101376-101387.
[14] Zanvettor, Giovanni Gino, et al. "A stochastic approach for EV charging stations in demand response programs." Applied Energy 373 (2024): 123862. (use receding horizon)
[15] Mesbah, Ali, et al. "Fusion of machine learning and MPC under uncertainty: What advances are on the horizon?." 2022 American Control Conference (ACC). IEEE, 2022.
[16] Zhang, Chiyuan, et al. "A study on overfitting in deep reinforcement learning." arXiv preprint arXiv:1804.06893 (2018).
[17] James, Steven, George Konidaris, and Benjamin Rosman. "An analysis of monte carlo tree search." Proceedings of the AAAI Conference on Artificial Intelligence. Vol. 31. No. 1. 2017.
[18] Nassef, Ahmed M., et al. "Review of metaheuristic optimization algorithms for power systems problems." Sustainability 15.12 (2023): 9434.[
[19] Christensen et al. (2025), A scoping review on electric vehicle charging strategies with a technical, social, and regulatory feasibility evaluation.
[20] Di et al. (2014), Electric vehicles charging control in a smart grid: A model predictive control approach
[21] Yang et al. (2023), EV charging scheduling under demand charge: A block model predictive control approach.
[22] He et al. (2022), Optimal integration of Vehicle to Building (V2B) and Building to Vehicle (B2V) technologies for commercial buildings.
[23] Ghosh et al. (2017), Control of charging of electric vehicles through menu-based pricing.
[24] Zeng et al. (2021), Inducing Human Behavior to Maximize Operation Performance at PEV Charging Station
References